## Slide 1
IoT Home Automation
& Safety System
ESP32-S3 · Gas Detection · Smart Lock · Water Management
Frais Asghar · 516900
SMME, NUST · ME-16 · Section A
Session 2024–2028
🔥 Gas Detection
💧 Water Mgmt
🔒 Smart Lock
Notes: Title slide. Introduce the project: IoT-based smart home automation using ESP32-S3. Mention three subsystems: gas detection, smart door lock, and automated water management.

## Slide 2
Problem Statement
Security gaps
Physical keys are easily lost, duplicated, or forgotten — creating security lapses when homeowners are away.
Safety hazards
LPG and CO gas leaks remain undetected until dangerous concentrations accumulate — posing severe fire and health risks.
Resource wastage
Manual water tank monitoring leads to dry pump runs (equipment damage) or overflow (water loss and electricity waste).
Notes: Three critical vulnerabilities in traditional home management: physical key security, silent gas hazards, and manual water monitoring causing waste or damage.

## Slide 3
Proposed Solution
ESP32-S3
Central Hub · Wi-Fi + BT
Smart Lock
SG90 servo · Wi-Fi + button · <100 ms
Gas Detection
MQ-2 · Buzzer + LED + Wi-Fi · <500 ms
Water Mgmt
HC-SR04 · Relay pump · <75 ms
Unified 3.3V Power Architecture · Common Ground
Notes: The ESP32-S3 acts as the central hub, connecting all three modules via a unified 3.3V architecture with integrated Wi-Fi for remote control and notifications.

## Slide 4
System Architecture & Pin Map
Pin | Component | Function | Signal
4 | HC-SR04 Trig | Water level trigger pulse | Digital OUT
6 | HC-SR04 Echo | Distance measurement | Digital IN
8 (ADC) | MQ-2 Gas Sensor | Gas concentration (LPG/CO) | Analog IN
9 (PWM) | SG90 Servo | Door lock actuation | PWM OUT
12 | Active Buzzer | Gas leak local alert | Digital OUT
14 | Relay LED | Pump relay simulation | Digital OUT
Power Architecture
ESP32-S3 (240 MHz)
HC-SR04
MQ-2 Gas Sensor
SG90 Servo
Active Buzzer
16×2 I²C LCD
3.3V · Common GND
Notes: Pin 8 is the ADC for gas sensing. Pin 9 drives PWM for servo control. Pins 4 and 6 are the ultrasonic trigger and echo. All on a single 3.3V rail.

## Slide 5
Module 1 — Gas Detection & Alert System
Sensor
MQ-2 (LPG, Smoke, CO)
Input Pin
Pin 8 — ADC
Threshold
400 ADC units
Poll rate
Every 500 ms
Response
450–520 ms
Accuracy
98% (< 2% false positive)
Tier 1 — Local
Buzzer (Pin 12) + Red LED — instant audible & visual
Tier 2 — Visual
LCD displays live gas ADC value and ALERT status
Tier 3 — Remote
Wi-Fi push notification to user smartphone with gas levels
Notes: Three-tier alert: local buzzer and LED, LCD display update, and remote Wi-Fi notification. Detection threshold of 400 ADC units with 98% accuracy.

## Slide 6
Module 2 — Automated Water Management
How it works
1
ESP32 sends TRIG pulse → Pin 4
2
HC-SR04 measures echo return time → Pin 6
3
Distance calculated using speed of sound (343 m/s)
4
If distance > 10 cm → LOW water → relay ON
5
Tank fills until distance ≤ threshold (80% full)
6
Relay turns OFF → pump stops → overflow prevented
±2 cm
Measurement accuracy
< 75 ms
Pump shutoff latency
< 100 ms
Pump activation latency
80%
Fill capacity threshold
Notes: The water management module uses closed-loop ultrasonic feedback. Pump activates when distance exceeds 10 cm, turns off at 80% full. Accuracy ±2 cm.

## Slide 7
Module 3 — Smart Door Lock System
🔒 LOCKED
Servo at 0°
🔓 UNLOCKED
Servo at 90°
OPEN cmd / button →
← CLOSE cmd / button
Mobile App (Wi-Fi)
OPEN or CLOSE command sent over local Wi-Fi to ESP32
Physical Button
Push button toggles door state on each press
Feedback & LCD
ESP32 confirms servo position; LCD always shows current door state
< 100 ms
Response time
90°
Unlock angle
10,000
Cycles tested
0
Overshoot
Notes: SG90 servo on Pin 9 (PWM). Two input methods: mobile app over Wi-Fi and physical button. Response under 100ms. 10,000 cycles with zero degradation.

## Slide 8
Implementation Phases
01
Breadboard Prototype
830-point solderless board
ESP32 ↔ mobile Wi-Fi verified
200+ servo calibration cycles
MQ-2 gas sensitivity tested
Filtering capacitors added
02
Proteus Simulation
Digital twin of full circuit
All 3 modules simulated live
Critical flyback diode issue found
Virtual oscilloscope timing analysis
Worst-case stress tests passed
03
Vero Board PCB
95% space utilisation
Analog/digital GND separated
Decoupling caps ≤5mm of VCC pins
No hotspot > 60°C (thermal sim)
2mm min trace separation
Notes: Three engineering phases: breadboard prototyping for hardware validation, Proteus simulation for digital twin testing (found critical relay spike issue), and final Vero board PCB.

## Slide 9
Results & Testing
PASS
Door Lock
< 100 ms
90° precision · zero overshoot · 10,000 cycles
PASS
Gas Detection
98% accuracy
450–520 ms · < 2% false positive rate
PASS
Pump Activation
< 100 ms
±1.5 cm threshold · from 0 to 1.5m height
PASS
Pump Shutoff
< 75 ms
Full-level detection · overflow prevention
Notes: All four test cases passed. Door lock: <100ms. Gas detection: 98% accuracy. Water pump activation: <100ms. Shutoff: <75ms. ±1.5cm threshold precision.

## Slide 10
Challenges & Solutions
!
Servo jitter during calibration
PWM duty cycle tuning required 200+ cycles to hit exact 90° without overshoot
✓ Multi-point PWM lookup table at 10° intervals with automated feedback loop
!
MQ-2 temperature drift
Gas sensor readings shifted with ambient temperature, raising false positive risk
✓ Adaptive thresholding based on temp readings — 2% accuracy across 0–50°C
!
Ultrasonic reflective noise
Vibrations and reflections produced erratic distance readings
✓ 20-sample moving average filter → 85% noise reduction, sub-500ms response
!
ESP32 resets from relay switching
Direct relay switching without flyback diodes caused voltage spikes on VCC
✓ 1N4007 flyback diodes + 100 µF bulk caps on relay terminals and ESP32 power pins
Notes: Four key engineering challenges: servo calibration jitter, MQ-2 drift, ultrasonic noise, and ESP32 reset from relay spikes. All resolved with targeted solutions.

## Slide 11
Bill of Materials
Component | Specs | Qty | PKR
ESP32-S3 | MCU, 240MHz, Wi-Fi+BT | 1 | 1,600
HC-SR04 | Ultrasonic, 2–400cm | 1 | 200
MQ-2 Sensor | Gas: LPG, Smoke, CO | 1 | 300
SG90 Servo | 180°, 5V PWM | 1 | 300
DC Mini Pump | 3–6V submersible | 1 | 200
16×2 I²C LCD | 5V module | 1 | 350
Buzzer + LED | Active 5V + Red 5mm | 1+1 | 60
Resistors/Pots | 100Ω / 1kΩ trimmers | 5 | 75
Breadboard + Vero | 830pt + PCB stripboard | 1+1 | 250
Misc | Solder, headers, wires | — | 300
TOTAL |  |  | 3235
Total Cost
₨ 3,235
~$11.50 USD
Source
ELECTROBES
Rawalpindi / Islamabad
Market Rates
Notes: Total BOM cost is ₨3,235 (approximately $11.50 USD). All components sourced from ELECTROBES in Rawalpindi and Islamabad.

## Slide 12
Conclusion & Future Scope
Conclusions
All 3 modules fully functional and tested
Systematic breadboard → simulation → PCB workflow demonstrated
Unified 3.3V architecture — compact and efficient
Cost-effective at ₨3,235 using commercial components
Scalable platform for real-world smart home deployment
Cloud logging
AWS IoT Core / Azure IoT Hub
Voice control
Alexa / Google Assistant
AC integration
Industrial relays + EM locks
On-device ML
TensorFlow Lite — anomaly detection
Notes: All objectives achieved. Future enhancements include cloud logging, voice control, AC circuit integration, and on-device TensorFlow Lite anomaly detection.