## Slide 1
3
Modules
±2cm
Accuracy
98%
Detection
PROTEUS PROFESSIONAL SIMULATION
PHASE 2
Proteus Software
Simulation
IoT-Based Smart Home
Automation and Safety System
Digital twin validation of hardware design, testing all three modules simultaneously in Proteus Professional environment before permanent PCB implementation.

## Slide 2
Why Proteus Simulation?
Validating hardware logic before permanent soldering — the smart way to engineer.
Risk Elimination
Catch voltage spikes, ground loops, and logic errors before any physical component is soldered.
Critical Issue Found
Discovered that direct relay switching without flyback diodes caused ESP32 reset events — fixed in final PCB design.
Virtual Oscilloscope
Enabled precise PWM timing analysis to reduce servo jitter and optimize frequency — impossible on breadboard alone.
SIMULATION WORKFLOW
1
Breadboard
Validated
2
Replicated in
Proteus
3
Logic Flow
Verified
4
Issues Found
& Fixed
5
PCB Design
Finalised

## Slide 3
Proteus Circuit Schematic
Complete digital twin — all three modules wired and simulated simultaneously
ARDUINO
UNO
(ESP32 Logic
Simulated)
HC-SR04
Ultrasonic
MQ Gas
Sensor
SG90
Servo Motor
DC Motor
(Pump)
LED +
Buzzer
Push
Button
Pin 12 (Trig)
Pin 11 (Echo)
A1 (Gas)
Pin 8 (Motor)
Pin 6 (Servo)
Pin 7 (Button)
Pin 2 (Buzzer)
Pin 13 (LED)
PIN MAPPING
Component | Pin | Role
Ultrasonic (Trig) | 12 | Water level trigger
Ultrasonic (Echo) | 11 | Distance feedback
Gas Sensor | A1 | LPG / CO detection
DC Motor | 8 | Pump simulation
Servo (Door) | 6 | Lock / Unlock
Push Button | 7 | Manual door control
LED | 13 | Gas alert visual
Buzzer | 2 | Gas alert audio
All components unified on 3.3V power rail with common ground — compact, stable circuit design.

## Slide 4
Simulation Validation Results
All three modules tested simultaneously — functional, stress, and edge-case scenarios
PASSED
Smart Door Lock
✓ 90 deg servo rotation
✓ < 95ms lock/unlock cycle
✓ No overshoot or jitter
PASSED
Gas Leak Detection
✓ 450-520ms alert response
✓ Buzzer + LED + Wi-Fi alert
✓ < 2% false positive rate
PASSED
Water Level Control
✓ ±2 cm threshold accuracy
✓ Pump ON > 10cm distance
✓ < 75ms pump response
VIRTUAL TERMINAL — SERIAL MONITOR OUTPUT
===========================================
SMART HOME AUTOMATION SYSTEM
Gas Threshold: 400 | Distance Threshold: 10 cm
Pump ON when distance > 10 cm
===========================================
Distance: 80 cm | Gas: 216 | LED: OFF | Buzzer: OFF | Pump: ON | Door: UNLOCKED
Distance: 78 cm | Gas: 216 | LED: OFF | Buzzer: OFF | Pump: ON | Door: UNLOCKED
Distance: 10 cm | Gas: 216 | LED: OFF | Buzzer: OFF | Pump: OFF | Door: UNLOCKED
RESPONSE TIME (ms)
Chart: 
| Door Lock | Gas Alert | Pump ON | Pump OFF
Latency (ms) | 95 | 485 | 85 | 68

## Slide 5
Key Findings & Simulation Impact
What Proteus revealed — and how each issue was resolved before PCB manufacturing
Direct relay switching caused voltage spikes that reset the ESP32 intermittently
Added 1N4007 flyback diodes across relay coils and 100µF bulk capacitors near power pins
Servo produced audible noise and showed timing jitter during PWM generation
Oscilloscope analysis revealed optimal PWM frequency; servo response latency minimised
Ground loops identified between analog sensor paths and digital relay control paths
Separated analog and digital ground planes at ESP32 reference — zero crosstalk in final PCB
Buzzer timing offset detected — triggered 80ms after threshold crossed
Logic flow corrected; all three modules now trigger simultaneously within specified windows
ISSUE FOUND IN SIMULATION
SOLUTION APPLIED TO PCB